## Slide 1: The Concept of Quality of Service in the Internet
Geoff Huston
APNIC
November 2013

## Slide 2
“With the move from traditional networks (based on dedicated service-channels and/or separate networks for each service) to integrated (transport) services on a single packet-based transport infrastructure, pre-defined transmission planning of Quality of Service (QoS) has become a major challenge, since many IP-based networks might not provide for self-standing end-to-end QoS, but only transport classes, which enable QoS differentiation. IP-based networks can support end-to-end QoS if the routers in between support the mechanisms and the network is designed for QoS.”

## Slide 3: A little while ago...
“Regardless of whether you are trying to implement QoS in a private network, or
within a segment of the global Internet, QoS comes at a cost. There is no magic here.”

## Slide 4: A little while ago...
“Regardless of whether you are trying to implement QoS in a private network, or
within a segment of the global Internet, QoS comes at a cost. There is no magic here.”

## Slide 5: Round 2:
QoS: “Caveat Emptor”

## Slide 6: Voice Networks
300 – 3500 Hz
Most of the energy is below 1Khz
Dynamic range of 50db

## Slide 7: Voice Networks
300 – 3500 Hz
Most of the energy is below 1Khz
Dynamic range of 50db
Digitization:
8000 samples / second
65,000 discrete levels
A-law encoding reduces this to 256 levels
64Kbps real time bitstream

## Slide 8: Digital Voice Networks
64K bitstreams
Tightly defined service
Jitter and drop intolerant
Synchronous networking
Multiplexing via strict time switching
End-to-end synchronous virtual circuits
Fixed total capacity
Networks engineered to peak load profile
Inefficient resource utilization
High precision clocking
Networks are costly to run
Network Services are expensive!

## Slide 9: Data Networks
Point-to-point Virtual Circuits
Network defined capacity
Synchronous bitstream services
Early data protocols borrowed many concepts from the voice network’s functions:

## Slide 10: Packet Networks
Computers are far more versatile than humans:
Packet Data network requirements:
Stateless packet switching
Unreliable packet service
Variable speed rates for data
Highly adaptive
Error tolerant
Jitter tolerant
Delay tolerant
Networks engineered to sustained load profile
efficient resource utilization
Networks are cheaper to run
Network Services are cheap!
Adaptive load demands
No requirement for central network resource management

## Slide 11
Services are cheap!
Services are expensive!
The Evolution of the Common Network Platform Model

## Slide 12
But different services need different treatment… don’t they?
Bulk Data Transfer - loss tolerant, jitter tolerant, adaptive speed
Web Systems – delay intolerant, jitter tolerant
Voice Services – delay intolerant, loss intolerant, jitter intolerant, fixed speed
Streaming Video Services – loss intolerant, fixed speed

## Slide 13
Bulk Data Transfer - loss tolerant, jitter tolerant, adaptive speed
But different services need different treatment… don’t they?
Web Systems – delay intolerant, jitter tolerant
Voice Services – delay intolerant, loss intolerant, jitter intolerant, fixed speed
Streaming Video Services – loss intolerant, fixed speed
Congestion prone!
Congestion intolerant!
Congestion intolerant!

## Slide 14
How can you efficiently mix congestion-prone and congestion intolerant applications within a single network platform?

## Slide 15
How can you efficiently mix congestion-prone and congestion intolerant applications within a single network platform?
Add more bandwidth!

## Slide 16
How can you efficiently mix congestion-prone and congestion intolerant applications within a single network platform?
Add more bandwidth!
Too easy!

## Slide 17
How can you efficiently mix congestion-prone and congestion intolerant applications within a single network platform?
Add more bandwidth!
Change the adaptive behaviour of the applications
Too easy!

## Slide 18
How can you efficiently mix congestion-prone and congestion intolerant applications within a single network platform?
Add more bandwidth!
Change the adaptive behaviour of the applications
Too easy!
Too hard!

## Slide 19
How can you efficiently mix congestion-prone and congestion intolerant applications within a single network platform?
Add more bandwidth!
Add resource management functions to the network
Change the adaptive behaviour of the applications
Too easy!
Too hard!

## Slide 20: The Goldilocks Procedure!
How can you efficiently mix congestion-prone and congestion intolerant applications within a single network platform?
Add more bandwidth!
Add resource management functions to the network
Change the adaptive behaviour of the applications
Too easy!
Too hard!
Just right! (supposedly)

## Slide 21: IP QoS -- Version 1
Integrated Services
Application
Network++
Resource
Reservation
Confirmation
Carriage
Release
(Network equipped with admission control, virtual circuits and resource reservation capability)

## Slide 22: “Integrated Services”
Adds the concept of a “flow state” into the network
The network must distribute a resource reservation along a static (“pinned”) flow path

## Slide 23: “Integrated Services”
Adds the concept of a “flow state” into the network
The network must distribute a resource reservation along a static (“pinned”) flow path
This creates within the data network:
state
+ complexity
+ fragility
= COST!

## Slide 24: “Integrated Services”
Adds the concept of a “flow state” into the network
The network must distribute a resource reservation along a static (“pinned”) flow path
This creates within the data network:
state
complexity
fragility
COST!
This form of QoS architecture simply does not scale!

## Slide 25: IP QoS -- Version 2
Differentiated Services
Application
Network
Admission
Control
Aggregate Service Types

## Slide 26: “Differentiated Services”
This is a pretty simple rerun of the TOS packet painting approach
It’s stateless, so it has more potential to scale to larger networks

## Slide 27: “Differentiated Services”
This is a pretty simple rerun of the TOS packet painting approach
It’s stateless, so it has more potential to scale to larger networks
But DiffServe service outcomes are relative, not absolute
And there is no effective form of feedback control to monitor the outcomes that the network is providing

## Slide 28: “Differentiated Services”
What is DiffServe attempting to tinker with?
Network
Carriage
Efficiency
Blindingly fast
Time for a cup of tea
Network Load
Best Effort Service Response
QoS Differential
Service Response
The QoS margin is
often quite a small
margin between unloaded
and catastrophically
overloaded
No marginal gain
The overloaded
abyss of despair!

## Slide 29: “Differentiated Services”
This is a pretty simple rerun of the TOS packet painting approach
It’s stateless, so it has more potential to scale to larger networks
But DiffServe service outcomes are relative, not absolute
And there is no effective form of feedback control to monitor the outcomes that the network is providing
Can’t perform per-flow resource reservations
Can’t deliver assured outcomes
Can’t guarantee fixed service response
Can’t see it and can’t measure it!
So who is prepared to pay for it?

## Slide 30: And so on and so on...
NSIS effort to standardise the signalling protocol between the application and the network for diffserve
MPLS as the elastic QoS band aid!
“Aggregated QoS” as an amalgam of Intserv and Diffserve, achieving none of either!

## Slide 31: IP QoS
Balancing Cost and Benefit:
  Simple QoS mechanisms can be supported in small scale enterprise environments
  But as you try to scale up the QoS approach the cost rapidly increases and the relative benefits decrease
  It becomes a skewed exercise of spending 95% of your engineering budget to secure less than 1% of your revenue!

## Slide 32: Why is IP QoS a Failure?
QoS does not create more network resources or a faster network
It just attempts to redistribute damage!
No magic here!

## Slide 33: Why is IP QoS a Failure?
QoS does not create more network resources or a faster network
It cannot fix:
over subscription
buffer bloat and congestion
poor network design
poor business plans
continental drift
gravity
the speed of light
No magic here!

## Slide 34: Why QoS?

## Slide 35: Why QoS?
Why is ETNO so keen on QoS?

## Slide 36: Why QoS?
Why is ETNO so keen on QoS?
  Because QoS appears to offer network operators increased visibility and the possibility of control over traffic flows that are passed over their networks

## Slide 37
Back to networking basics....

## Slide 38
The historical vertically integrated service architecture
Telco nostalgia...
Users
$

## Slide 39
Devolution of the integrated
service architecture through
an open IP service architecture
and deregulation
Deregulation

## Slide 40
Devolution of the integrated
service architecture
Where’s the money to invest
in new network services?

## Slide 41
Users
Services
Access Provider

## Slide 42
Users
Services
G
L
A
Services-facing QoS provide control points in the IPv4 network that allow monetary extraction from both consumers and content providers
Q
o
S
Q
o
S
Access Provider

## Slide 43: Why QoS?
Why is this control important?
  Because network operators believe that this will allow them to extort revenue from content service providers

## Slide 44: Why QoS?
Why appeal to the ITU to mandate inter-provider IP QoS into the ITRs?
  Because when you are stuck with an unattractive business plan and you want to address this by generating an unnatural outcome in the market, there is nothing quite like having regulatory impost on your side!

## Slide 45: Goldilocks was wrong!
How can you efficiently mix congestion-prone and congestion intolerant applications within a single network platform?
Add more bandwidth!
Add resource management functions to the network
Change the adaptive behaviour of the applications
Current Operational Practice!
Active Research Topic
Too hard!

## Slide 46: Thank You!